Code Walkthrough
In this section, we will walk through each and every line of the BME280 code, explaining what each step does. Read at your own pace, and ask the instructors if you have any questions.

#include <SPI.h>
#include <Adafruit_Sensor.h>
#include <Adafruit_BME280.h>

We start by pulling in the library for running the SPI interface. Next, we import some ibraries from the manufacturer used for all of their sensors. Finally, we pull in the library from the manufacturer to run this BME280 sensor.

int chipSelect = 10;
float sealevel = 1013.25;
Adafruit_BME280 bme(chipSelect);

First we create a variable, of type integer which represents the chipSelect pin used to select the BME280. We assign this variable the value of 10. Next, we create a variable of type floating point that represents the pressure (in kPa) at sea level. This will be used later in the program to calculate altitude. Finally, we create a variable to hold the BME280 library code, and we tell it on which pin it will find the chip select.

void setup() {
    Serial.begin(9600);
    Serial.println("initializing BME280...");
    if (!bme.begin()) {
        Serial.println("BME280 Failed or Not Present");
        while (1);
    }
    Serial.println("...BME280 initialized");
    delay(1000);
}

In the setup function we start by initializing the serial interface and printing an initialization message. We then begin the BME280; if successful we print a success message and continue. If unsuccessful, we print a failure message and stop. We wait 1 second to give the device time to initialize completely.

void loop() {
    Serial.print("Temperature: ");
    Serial.print(bme.readTemperature());
    Serial.println(" C");

    Serial.print("Pressure: ");
    Serial.print(bme.readPressure());
    Serial.println(" Pa");

    Serial.print("Altitude: ");
    Serial.print(bme.readAltitude(sealevel));
    Serial.println(" m");

    Serial.print("Humidity: ");
    Serial.print(bme.readHumidity());
    Serial.println(" %");

    Serial.println();
    delay(1000);
}
In the loop function, we print to the serial monitor the values of the various properties the BME280 measures. In each case, we print some text around the value itself so we can read what it represents. In each case, we finish with println to add a new line before printing the next property. Reading the temperature, pressure and humidity are all very straight foward. Reading the altitude requires some input in the form of the presssure at sea level, which we defined earlier in the sketch.